SECTION 271116 - COMMUNICATIONS CABINETS, RACKS, FRAMES, AND ENCLOSURES

PART 1 - GENERAL

1.1	RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 01 Specification Sections, apply to this Section.

1.2	SUMMARY

Section Includes:

1.	E Series Cabinet

1.3	DEFINITIONS

A.	BICSI: Building Industry Consulting Service International

B.	EIA:  Electronic Industries Alliance.

C.	TIA: Telecommunications Industry Association.

D.	ANSI: American National Standard Institute.

E.	LAN: Local area network.

F.	RCDD: Registered Communications Distribution Designer.

1.4	REFERENCES

A.	ANSI/TIA-569-D Telecommunications Pathways and Spaces, 2015

B.	ANSI/TIA-568-D.0 Generic Telecommunications Cabling for Customer Premises, 2015

C.	ANSI/TIA – 568-D.1 Commercial Building Telecommunications Cabling Standard, 2015.

D.	ANSI/NECA/BICSI 568-2006 – Standard for Installing Commercial Building Telecommunications Cabling.

E.	ANSI/TIA-942-A Telecommunications Infrastructure Standard for Data Centers, 2014.

F.	ANSI/TIA – 606-B Administration Standard for Telecommunications Infrastructure, 2012.

G.	ANSI/TIA – 607-C Generic Telecommunications Bonding and Grounding (Earthing) For Customer Premises, 2015.

H.	ANSI/NFPA 70 – National Electric Code, 2008, 2014.

1.5	ACTION SUBMITTALS

A.	Product Data: For each type of product.

1.	Include construction details, material descriptions, dimensions of individual components and profiles, and finishes for equipment racks and cabinets.

2.	Include rated capacities, operating characteristics, electrical characteristics, and furnished specialties and accessories.

B.	Shop Drawings: For communications equipment room fittings.

1.	Include plans, elevations, sections, details, and attachments to other work.

2.	Detail equipment assemblies and indicate dimensions, weights, loads, required clearances, method of field assembly, components, and location and size of each field connection.

3.	Equipment Racks and Cabinets: Include workspace requirements and access for cable connections.

4.	Grounding: Indicate location of bonding bus bar and its mounting detail showing standoff insulators and wall mounting brackets.

1.6	INFORMATIONAL SUBMITTALS

A.	Qualification Data: For [Installer] qualified layout technician, installation supervisor, and field inspector.

B.	Seismic Qualification Certificates: For equipment frames from manufacturer.

C.	Basis for Certification: Indicate whether withstand certification is based on actual test of assembled components or on calculation.

1.	Dimensioned Outline Drawings of Equipment Unit: Identify center of gravity and locate and describe mounting and anchorage provisions. Base certification on the maximum number of components capable of being mounted in each rack type. Identify components on which certification is based.

2.	Detailed description of equipment anchorage devices on which the certification is based and their installation requirements.

1.7	QUALITY ASSURANCE

A.	Installer Qualifications: Cabling Installer must have personnel certified by BICSI on staff.

B.	Layout Responsibility: Preparation of Shop Drawings shall be under the direct supervision of [RCDD] [RCDD/NTS] [Commercial Installer, Level 2].

1.	Installation Supervision: Installation shall be under the direct supervision of [Registered Technician] [Level 2 Installer], who shall be present at all times when Work of this Section is performed at Project site.

2.	Field Inspector: Currently registered by BICSI as [RCDD] [Commercial Installer, Level 2] to perform the on-site inspection.

PART 2 - PRODUCTS

2.1	E SERIES DATA RACKS

Basis-of-Design Product: Subject to compliance with requirements, provide Great Lakes Data Racks & Cabinets (GLDRC); ES SERIES Rack.

Color: Black textured powder coated steel

UL 2416 Listed: 1500 lb. capacity, static

Constructed cold rolled steel

Welded frame #16ga. & #14ga. Horizontal rails

2 pair mounting rails #12ga.

Top panel #16ga.

Doors and side panel #16ga.

Front door: Round mesh with keyed locking swing handle; all doors with field reversible hinges

Lift off hinge type, with bonding wire and quick disconnect

Handle cutout, 25mm x 150mm

Rear door: Round mesh with keyed locking swing handle; all doors with field reversible hinges

Lift off hinge type, with bonding wire and quick disconnect

Handle cutout, 25mm x 150mm

Side panels: Two solid sides with keyed lock

Top of Cabinet Frame, Cable Access: No cable access locations on top of frame

Top Panel: Removable; Solid with two 4" horseshoe knockouts for cable access

Bottom Panel: Removable; Optional: Solid; Brush; Filtered

Mounting Rails: Two pair of 3/8” (M6) Square Hole with RMU ascending labels; rails feature Flexible Mounting Profile (FMP) for zero-U accessory mounting; support 19” EIA equipment

Leveling Glides: qty-4, installed

Casters: Optional: Stem casters, 2 locking and 2 non-locking

Power Strip Mounting: Optional: Pair of Adjustable Height Brackets, for button mounting

Optional Internal Cable Management

Horizontal and Vertical Cable Bars

Vertical Cable Trough, with Hinged cover & Zero U Mtg. options

Plastic Cable separation fingers, 4” & 7” long options

Optional mounting to front or rear of EIA Rail

Cable rings, Metal with Cable Lacing slots

Optional mounting to front or rear of EIA Rail

Optional Air Flow Accessories

19” Stationary fan tray, 19” Adjustable fan tray

Top panel with fan assembly: 550 CFM top panel, 1100 CFM top panel, 225 CFM top panel

Rack Mounting Units (RMU) numerically labeled in ascending order, bottom to top

Country of Origin, Made in the USA

RMU Height: 44 RMU, 84”

Width: 24”

Depth: 32”

B.	MODEL NUMBER

1)	GL840E-2432-B-SQM6MS

PART 3 - EXECUTION

3.1	INSTALLATION OF FLOOR MOUNTED EQUIPMENT RACKS

- Assemble racks according to manufacturer's instructions. Verify that equipment mounting rails are sized properly for rack-mount equipment.

- Racks shall be grounded to the bonding busbar using appropriate hardware provided by the contractor. The bond will meet local code requirements and will be approved by the Authority Having Jurisdiction (AHJ).

- Ladder rack may be attached to the top of the rack to deliver cables to the rack. The rack shall not be drilled to attach ladder rack. Use appropriate hardware from the ladder rack manufacturer.

- The equipment load will be evenly distributed and uniform on the rack. Place large and heavy equipment towards the bottom of the rack. Secure all equipment to the rack with equipment mounting screws. In seismic areas, secure equipment to shelves with additional bracing.

- Accessory Equipment Mounting Rails:  Equipment must be attached to the equipment mounting rails and must not exceed the accessory equipment mounting rails load capacity.  Verify that the rack has sufficient load capacity for the accessory equipment mounting rails and equipment.

- Shelves:  Equipment placed on the shelf must fit completely within the shelf surface and must not exceed the shelf load capacity.  Verify that the rack has sufficient load capacity for the shelf and equipment.

END OF SECTION 271100

Additional E Cabinets Available
Note that actual part numbers are not listed below. To configure an E cabinet, visit GreatCabinets.com

- GL300E-2432 13 RMU, 30"H; 19" EIA assembly, 24" W, 32” D

- GL480E-2432 24 RMU, 48"H; 19" EIA assembly, 24" W, 32” D

- GL600E-2432 31 RMU, 60"H; 19" EIA assembly, 24" W, 32” D

- GL720E-2432 37 RMU, 72"H; 19" EIA assembly, 24" W, 32” D

- GL720E-2436 37 RMU, 72"H; 19" EIA assembly, 24" W, 36” D

- GL720E-2932 37 RMU, 72"H; 19" EIA assembly, 29" W, 32” D

- GL720E-2936 37 RMU, 72"H; 19" EIA assembly, 29" W, 36” D

- GL840E-2432 44 RMU, 84"H; 19" EIA assembly, 24" W, 32” D

- GL840E-2436 44 RMU, 84"H; 19" EIA assembly, 24" W, 36” D

- GL840E-2932 44 RMU, 84"H; 19" EIA assembly, 29" W, 32” D

- GL840E-2936 44 RMU, 84"H; 19" EIA assembly, 29" W, 36” D